| Mixed commercial market in Colibasi village, Cahul rayon Update 03.2022 | Form No. 1 |
| --- | --- |
| (name of the site) |  |

List with quantities of works No. 2-1-1

Architectural solutions (03/2021-1-SA)

Type of works

Bid currency -  USD

| No crt. | Symbol of the norm and resource code | Name of works | Unit of measure | Volume |
| --- | --- | --- | --- | --- |

| 1 | 2 | 3 | 4 | 5 |
| --- | --- | --- | --- | --- |
|  |  | Chapter 1. Demolishing works |  |  |
| 1 | RpCG29C1 | Demolishing with mechanical means the full brick walls, autoclaved aerated concrete, clay or light concrete blocks, perforated bricks, except for scaffold and cleaning the bricks for demolishing with mechanical means at the roof | m3 | 4.00 |
| 2 | RpCJ35A | Dismantling the interior plastering from the ceilings | m2 | 156.00 |
| 3 | RpCJ35A | Dismantling the plastering from walls | m2 | 560.00 |
| 4 | RpCI42F | Removing roof elements – bitumen membranes | m2 | 160.00 |
| 5 | RpCK42A | Dismantling the cement mortar screed from the roof | m2 | 160.00 |
| 6 | RpIzC45B | Removing the insulating materials from the roof: granular coating (granules or similar) | m3 | 32.00 |
| 7 | RpVB40A | Dismantling the circular deflectors D=500 mm | pcs | 1.00 |
| 8 | RpCB18G | Demolishing the old concrete by mechanic means, reinforced concrete - foundation for the boiler | m3 | 0.80 |
| 9 | RpCG29C1 | Demolishing with mechanical means the full brick walls, autoclaved aerated concrete, clay or light concrete blocks, perforated bricks, except for scaffold and cleaning the bricks for demolishing with mechanical means inside the premises | m3 | 9.60 |
| 10 | RpCK42A | Dismantling the cold flooring from concrete or cement mortar | m2 | 141.40 |
| 11 | TsH92B | Loading soil with stones and boulders in trucks | t | 153.30 |
| 12 | TsI51A10 | Transportation of soil with the dumper of 10 t at a distance of 10 km | t | 153.30 |
|  |  | Chapter 2. Internal finishing works |  |  |
|  |  | Chapter 2.1. Flooring |  |  |
| 13 | CA04A3 | Cast concrete slabs , beams , columns , prepared with the concrete plant and pouring with classical means of reinforced concrete Class C 10/8 ( Bc 10 / B 150 ) at heights up to 35 m inclusively | m3 | 8.28 |
| 14 | CG01A | Supporting layer for flooring executed from cement mortar M 100-T of 3 cm thickness with delicately smoothed surface | m2 | 165.60 |
| 15 | IzF31A | Waterproofing the concrete surfaces (vertical ones, horizontal ones, including the ceilings) with “Penetron” mixture - 2 layers: smooth surface | m2 | 165.60 |
| 16 | CG01A | Supporting layer for flooring executed from cement mortar M 100-T of 3 cm thickness with delicately smoothed surface | m2 | 165.60 |
| 17 | CN53A | Coating the internal surfaces with the primer based on quartz sand | m2 | 165.60 |
| 18 | CG17D | Flooring from NON-SLIP porcelain plates including the support layer from adhesive mortar, executed on areas wider than 16 m2 | m2 | 165.60 |
| 19 | CI14A | Linear elements of stoneware plates applied with adhesive | m | 67.90 |
|  |  | Chapter 2.2. Ceilings |  |  |
| 20 | СF59D | Coating the surfaces with a layer of water-resistant plasterboards 12.5 mm thick, executing the simple plain metallic carcass with CW50 and UW50 profiles, with the height up to 4 m: ceilings without insulation | m2 | 13.22 |
| 21 | CF52B | Interior coating of 5 mm thickness, executed manually, with gypsum-based dry mixture, for the ceiling, manual preparing of the mortar | m2 | 152.36 |
| 22 | CF53B k=5 | Interior coating of 5 mm thickness, executed manually, with gypsum-based dry mixture, for the ceiling, manual preparing of the mortar The plus or minus difference for every 1.0 mm (is added or extracted at art. CF52) | m2 | 152.36 |
| 23 | CF17C | Fiberglass layer with a weight of 80 gr / m2, applied in the composition of the plaster with the dry mix | m2 | 152.36 |
| 24 | CF57A | Manual application of the gypsum-based putty, thickness 1,0 mm on the ceiling, walls and columns’ areas. | m2 | 165.58 |
| 25 | CF56A | Manual application of the putty for interior works thickness 0,5 mm on the surfaces of walls, columns, and ceilings | m2 | 165.58 |
| 26 | CN53A | Coating the internal surfaces of the walls and ceilings | m2 | 165.58 |
| 27 | CN06A | Interior painting with paints based on vinyl copolymers in water emulsion, applied in 2 layers on the existing fillings, executed manually. | m2 | 165.58 |
|  |  | Chapter 2.3. Walls |  |  |
| 28 | CF02B | Interior coating of 2 cm thickness, levelled, executed manually, on the walls or columns, on plain surfaces, with cement-lime mortar M 100-T brand, for sprit, ground and visible layer, on brick masonry or small blocks of concrete | m2 | 283.94 |
| 29 | CN53A | Coating the internal surfaces with the primer based on quartz sand | m2 | 234.39 |
| 30 | CI22B | Ceramic tile plywood (on walls, columns, pilasters and window sills) fixed with adhesive (dry mixture), plates’ dimensions: the size and color to be coordinated with the Beneficiary | m2 | 234.39 |
| 31 | CF50B | Interior coating of 5 mm thickness, executed manually, with cement-based dry mixture, for walls | m2 | 182.60 |
| 32 | CF17C | Fiberglass layer with a weight of 80 gr / m2, applied in the composition of the plaster with the dry mix | m2 | 182.60 |
| 33 | CF51B k=2 | Interior coating of 5 mm thickness, executed manually, with gypsum-based dry mixture, for walls and dividing walls, manual preparation of the mortar. The plus or minus difference for every 1.0 mm (is added or extracted for art. CF50) | m2 | 182.60 |
| 34 | CF57A | Manual application of the gypsum-based putty, thickness 1,0 mm on the ceiling, walls and columns’ areas. | m2 | 182.60 |
| 35 | CF56A | Manual application of the putty for interior works thickness 0,5 mm on the surfaces of walls, columns, and ceilings | m2 | 182.60 |
| 36 | CN53A | Coating the internal surfaces of the walls and ceilings | m2 | 182.60 |
| 37 | CN06A | Interior painting with paints based on vinyl copolymers in water emulsion, applied in 2 layers on the existing fillings, executed manually. | m2 | 182.60 |
|  |  | Chapter 2.4. Sanitary blocks partitioning |  |  |
| 38 | CK22D | French windows of molding made of aluminum profiles and HPL plating for sanitary groups, in premises with heights up to 35 m of door plates equipped with internal locks | m2 | 11.97 |
| 39 | CK22B | French windows of molding made of aluminum profiles and HPL plating for sanitary groups, in premises with heights up to 35 m of fixed plates | m2 | 13.44 |
|  |  | Chapter 3. Carpentry |  |  |
| 40 | CK25D1 | Doors made of plastic profiles, external, thermally insulated, with over-light, including the casement and the necessary accessories for assembling doors in any type of constructions with the height over 35 m, in two wings, with the surface of the case up to 7 m2 inclusively (U1-2 units). The color will be coordinated with the Beneficiary. | m2 | 9.76 |
| 41 | CK25A | Doors made of plastic profiles, external, thermally insulated, including the casement and the necessary accessories for assembling doors in any type of masonry in constructions with the height up to 35 m inclusively, in one leaf, with the surface of the case up to 7 m2 inclusively (U2-1 unit). The color will be coordinated with the Beneficiary. | m2 | 2.10 |
| 42 | CK03C | Wooden interior doors in two leaves, on coating and balcony doors, including thermal and waterproof casement, assembled on the existing dowels of the constructions with height up to 35 m (U3-1 unit). The color will be coordinated with the Beneficiary. | m2 | 2.64 |
| 43 | CK03A | Interior doors from MDF, in one leaf, resistant to moisture and painting, with smooth surface, including thermal insulation and waterproof of the casement, assembled on the existing dowels of the constructions with height up to 35 m (U4-5 units). The color will be coordinated with the Beneficiary. | m2 | 9.45 |
| 44 | CK03A | Interior doors from MDF, in one leaf, resistant to moisture and painting, with smooth surface, including thermal insulation and waterproof of the casement, assembled on the existing dowels of the constructions with height up to 35 m (U5-2 units). The color will be coordinated with the Beneficiary. | m2 | 2.94 |
| 45 | CK25A | Doors made of plastic profiles, external, thermally insulated, including the casement and the necessary accessories for assembling doors in any type of masonry in constructions with the height up to 35 m inclusively, in one leaf, with the surface of the case up to 7 m2 inclusively (U6-1 unit). The color will be coordinated with the Beneficiary. | m2 | 2.10 |
| 46 | CK25A | Doors made of plastic profiles, external, thermally insulated, including the casement and the necessary accessories for assembling doors in any type of masonry in constructions with the height up to 35 m inclusively, in one leaf, with the surface of the case up to 7 m2 inclusively (U7-2 units). The color will be coordinated with the Beneficiary. | m2 | 3.52 |
| 47 | CK25A | Doors made of plastic profiles, external, thermally insulated, including the casement and the necessary accessories for assembling doors in any type of masonry in constructions with the height up to 35 m inclusively, in one leaf, with the surface of the case up to 7 m2 inclusively (U8-2 unit). The color will be coordinated with the Beneficiary. | m2 | 1.12 |
| 48 | CK33A | Automated device for closing the doors, with the weight up to 100 kg | pcs | 3.00 |
| 49 | CK33C | Yale system applied lock, including the handle, in the set with 5 keys | pcs | 11.00 |
| 50 | CK07B | MDF sills assembled on doors. The color will be coordinated with the Beneficiary | m | 56.50 |
| 51 | CK57E | Fitting windows made of PVC profiles with 5 chambers, class A, RAL, according to the color passport, with thermal bridge, heating transfer K=2.5 (W/m2K) with double glazing glass window, 4.0 mm thick: tilts (folding, swing-out) with more than 2 m2 of the opening area with 2 leaves, equipped with anti-insects mesh (F1 - 1 unit) | m2 | 1.65 |
| 52 | CK57E | Fitting windows made of PVC profiles with 5 chambers, class A, RAL, according to the color passport, with thermal bridge, heating transfer K=2.5 (W/m2K) with double glazing glass window, 4.0 mm thick: tilts (folding, swing-out) with more than 2 m2 of the opening area with 2 leaves, equipped with anti-insects mesh (F2 - 3 units) | m2 | 5.63 |
| 53 | CK57E | Fitting windows made of PVC profiles with 5 chambers, class A, RAL, according to the color passport, with thermal bridge, heating transfer K=2.5 (W/m2K) with double glazing glass window, 4.0 mm thick: tilts (folding, swing-out) with more than 2 m2 of the opening area with 2 leaves, equipped with anti-insects mesh (F3 - 2 units) | m2 | 1.28 |
| 54 | CK57E | Fitting windows made of PVC profiles with 5 chambers, class A, RAL, according to the color passport, with thermal bridge, heating transfer K=2.5 (W/m2K) with double glazing glass window, 4.0 mm thick: tilts (folding, swing-out) with more than 2 m2 of the opening area with 2 leaves, equipped with anti-insects mesh (F4 - 2 units) | m2 | 0.90 |
| 55 | CK26B | Sills assembled at the windows from aluminum | m | 9.40 |
| 56 | CK26C | Sills assembled on plastic windows with width, including installation of lateral plugs. The color will be coordinated with the Beneficiary | m | 9.40 |
|  |  | Chapter 4. Facade |  |  |
| 57 | CB14A | Tubular metallic scaffold for works on vertical areas for heights up to 30 m inclusively, with immobilization of the scaffold for 25 days (200 hours) | m2 | 502.00 |
| 58 | CK26B | Sills assembled at aluminum windows - 100mm aluminum base profile, with the modification in standards for Screws with notched head 6 x 30 mm on the resource Dowels with hexagon head screw 12x180 mm | m | 82.60 |
| 59 | CE23C | Sills made of galvanized sheet, with anticorrosive protection and RAL coverage, 0.5 mm thickness on a layer of roofing felt mounted on a equalization dig of cement - lime mortar -T M 100 , secured on break masonry, for lengths of more than 2 m, with width of 30 cm. | m | 82.60 |
| 60 | IzF55C | External thermal insulation of the walls of the buildings with fine plaster based on thermal insulators (rigid fixation systems of the thermal insulation), smooth wall surface: with plates of mineral wool with density 135 kg/m3 th, lambda - 0.038, thickness 100 mm | m2 | 426.00 |
| 61 | CN54B | Manual application of the quartz ground “Gleta" in one layer, for the exterior walls of the facade. | m2 | 426.00 |
| 62 | CF30A | Exterior coating of 2 mm thickness, executed manually, with decorative finishing material with silicone addition, on walls, white color | m2 | 426.00 |
| 63 | IzF01C | Priming the surface for applying diffusion layer, a barrier against steam, heat-insulation or waterproofing on ceilings of any form, with suspension of filtered bitumen modification (subif) in one layer (2 layers) | m2 | 105.00 |
| 64 | IzF55B | External thermal insulation of buildings’ walls with fine plaster based on thermal insulators (rigid fixation systems of the thermal insulation), smooth wall surface: with polystyrene plate | m2 | 105.00 |
| 65 | RpCJ10A | Repairing the external plastering of 3 cm thickness, executed on net VR1 d=3.0 mm with mesh 100x100 mm, leveled, on walls, with cement mortar, brand 100-T for HRMS, lime-cement mortar brand 50-T for primer and lime mortar brand 10-T for the visible layer, applied on walls | m2 | 53.00 |
| 66 | CN53A | Coating the internal surfaces with the primer based on quartz sand | m2 | 53.00 |
| 67 | CI22B | Concrete plywood plates (Cosauti stone type style) (for walls, columns, pilasters and window sills) fixed with adhesive for exterior works, size of the plates: up to 200 x 200 mm | m2 | 53.00 |
| 68 | CE41A | Assembling the decorative elements of the facade made of planed planks, section 100x40 (h) mm, with antiseptic treatment | m3 | 0.60 |
| 69 | CE41A | Assembling the decorative elements of the railing, made of planed planks, with antiseptic treatment | m3 | 0.37 |
| 70 | CN17A | Painting with alkyd raisins -based paints applied on the wooden carpentry, executed with 2 layers of alkyd enamel, including the primer | m2 | 68.00 |
|  |  | Chapter 5. Roof |  |  |
| 71 | IzF04J1 | Waterproofing layer made of floors made with diffusion barrier, simple, laid with non-stick overlays | m2 | 174.00 |
| 72 | IzF53A | Executing manually the flooring support with thermal-insulating layer made of plates with mineral wool, density 160 kg/m3, thickness 90 mm, lambda = 0.039 W/mK, in one layer | m2 | 174.00 |
| 73 | IzF53A | Executing manually the flooring support with thermal-insulating layer made of plates with mineral wool, density 160 kg/m3, thickness 100 mm, lambda = 0.039 W/mK, in one layer | m2 | 174.00 |
| 74 | IzF04J1 | Waterproofing layer made of floors made of Polyethylene film 100mk thick, simple, laid with non-stick overlays | m2 | 174.00 |
| 75 | IzF18C k=1.667 | Support layer for equalization or protective insulation, including related moldings, executed with ready-made mortar cement of M25 brand without any lime adds, leveled, on horizontal or inclined surfaces up to 40% inclusively, applied in medium thickness of 3 cm - 50 mm thick, k=1.667 | m2 | 174.00 |
| 76 | CE17A | Water-protective film layer with the following characteristics: breaking load N / 5> = 196; Water impermeability> 0.2 m water column; Working temperature -40 * C / + 80 * C; Resistance to ultraviolet rays> 4 months | m2 | 330.00 |
| 77 | CR03A | Strip of 50x30(h) mm of softwood planks | m3 | 1.37 |
| 78 | CE30A | Sheathing or valley flashing made of roofing tiles, Eternit type plates etc., softwood planks (50x50(h) mm thick, step 330 mm), used in ordinary constructions. | m2 | 330.00 |
| 79 | CN50C | Fireproofing treatment of the carpentry, stave-based screen for coverings and revetment. | 100 m2 | 3.78 |
| 80 | CN51K | Antiseptic treatment of the carpentry, on visible areas with water solution: coating the trusses. | 100 m2 | 3.78 |
| 81 | CE07A | Corrugated metal sheets (tile effect) for roof covering (Lindab type) RAL 7016 | m2 | 330.00 |
| 82. | CE22A | Systems of brass-type tubing from anticorrosive protected board D=100 mm, RAL 7016 | m | 22.00 |
| 83 | CE20A | Systems of brass-type ditches from anticorrosive protected board D=150 mm, RAL 7016 | m | 57.00 |
| 84 | CK26B | Installing the snow guards using anticorrosive protected 0.5 mm thick boards, B=220 mm, RAL 7016 | m | 79.00 |
| 85 | CE30A | Sheathing or valley flashing made of roofing tiles, Eternit type plates etc., softwood planks (50x50(h) mm thick, step 330 mm), used in ordinary constructions (source) | m2 | 15.60 |
| 86 | CE06C | Anticorrosive protected and profiled board covers, h=20 mm, thickness 0.45 mm, folded, RAL 7016, mounted on metal blades, executed on areas wider than 40 m2 with sheets of profiled board with self-tapping screws (on the upper flange of the metallic wedge) and consolidated with clenches, including the execution of valleys, aprons, connections to chimneys etc. (source) | m2 | 15.60 |
| 87 | CE31C | Clogged eaves without apparent consoles from pinewood planks folded and smoothed, with thickness of 12.5 mm | m2 | 79.80 |
| 88 | CN17A | Painting with alkyd raisins -based paints applied on the wooden carpentry, executed with 2 layers of alkyd enamel, including the primer | m2 | 79.80 |
|  |  | Chapter 6. Diverse |  |  |
|  |  | Chapter 6.1. Perforated halls |  |  |
| 89 | RCsB29N | Drilling holes in brick and stone masonry, using the machine with cutter with diamond drill core, diameter: 150 mm, L=400 mm, K=3.6 | pcs | 2.00 |
| 90 | RCsB29S k=3.989 | Drilling holes in brick and stone masonry, using the machine with cutter with diamond drill core, diameter: 200 mm, L=400 mm, K=3.989 | pcs | 3.00 |
| 91 | RCsB29S k=6.23 | Drilling holes in brick and stone masonry, using the machine with cutter with diamond drill core, diameter: 250 mm, L=400 mm, K=6.23 | pcs | 1.00 |
| 92 | RCsB30J k=1.08 | Drilling holes in concrete constructions of the brand up to 500, using the machine with cutter with diamond drill core, diameter: 110 mm, L=120 mm, K=1.0 | pcs | 2.00 |
| 93 | RCsB30S k=1.08 | Drilling holes in concrete constructions of the brand up to 500, using the machine with cutter with diamond drill core, diameter: 200 mm, L=120 mm, K=1.08 | pcs | 1.00 |
| 94 | RCsB30S k=2.97 | Drilling holes in concrete constructions of the brand up to 500, using the machine with cutter with diamond drill core, diameter: 315 mm, L=120 mm, K=2.97 | pcs | 2.00 |
|  |  | Chapter 6.2. Access stairs |  |  |
| 95 | TsA03B | Manual excavation of land in confined spaces, having under 1.00 m in width, made without support, with sloping embankment foundations, channels , etc., non-cohesive or slightly cohesive, consistent soil, up to 0.75 m deep, middle ground | m3 | 3.20 |
| 96 | TsC54C | Foundation layer of gravel | m3 | 2.50 |
| 97 | CA03C2 | Cast concrete slabs, beams, columns, support walls, prepared with the concrete plant on the site and pouring with classical means of reinforced concrete Class C 10/8 ( Bc 10/B 150 ) | m3 | 9.80 |
| 98 | CC01C | Concrete steel fittings A240 shaped in construction shops, assembled with bars over 8 mm diameter inclusively in insulated foundations | kg | 86.70 |
| 99 | CB03A | Reusable formwork panels with revetment of 15 mm for pouring the concrete in bearings, foundations and foundations glass and foundation equipment including support | m2 | 6.46 |
| 100 | CN53A | Coating the internal surfaces with the primer based on quartz sand | m2 | 31.96 |
| 101 | CG47C | Anti-slip ceramic, porcelain, tile floors, cold-resistant, including the support layer from adhesives for exterior works | m2 | 31.96 |
|  |  | Total Incl. salary | $ $ |  |
|  |  | Social Insurance, 24% | $ |  |
|  |  | Transportation costs, % | $ |  |
|  |  | Supply - storage costs, % | $ |  |
|  |  | Total | $ |  |
|  |  | Overhead costs, % | $ |  |
|  |  | Total | $ |  |
|  |  | Estimate benefit, % | $ |  |
|  |  | Total | $ |  |
|  |  | Total estimates: Incl. salary | $ $ |  |

Bidder

Certified estimates’ developer (position, signature, name, surname)

S.P.